Title	Trident_1-9_complementary_3dPartsBuild_doco (proposed future file)
File name	Voron_1.9_3dprinting_guide.pdf (1.9 – really? You put . in a file?)
Date	2021-12-15 AM (Unofficial version number)
Copy-rite	None. Free domain. Be free. Fly my pretties. FLY!
Warranty	None. Use at own risk. For entertainment purposes only.
Author(s)	Stephen George (Original idea and creation)
Claudermilk (Major proof read and error checking)

Introduction
Use this guide to print the parts as you need them, possibly the night before.

Latest version?
I tend to rush the first draft out and let everyone complain. To get the latest version of this document please goto (*1) and check the date.
(*1) https://github.com/LesserSpottedAustralianSquirel/voron_trident_pics/blob/main/Voron_1.9_trident_3dprinting_guide.pdf

Print parameters (More details on page 4 of official Trident manual)
Material ABS, Infill gyroid, Infill 40% Layer_height 0.2mm, Wall_count 4, Top/bottom layers 5, Nossle/Nozzle 0.4mm

NB: Many of the Voron parts “mate” together. Therefore the top needs to be quite smooth. I found that a light sand papering helped allow these parts to mate. Another idea was to enable “ironing” in your slicer. However this adds to the print time and has not been tested by me.

NB: I used a Prusa mini to print the parts in ABS. I had to use a brim to prevent warping. While this came off easily I had to use a plumbers deburring tool (from the hardware shop) and sometimes a craft knife to remove the elephants foot like effect.

The Rules
The first time a picture of the part is shown in the official instructions it should be added to the list below, along with the page number. After that it’s ignored as you should have already printed it.

The Machine the parts are for
Building Formbot kit, 250 x 250, Direct feed, Dragon High Flow, 3 hole cable chain.

Keeping track
The Printed ▢ tick box in the page number box allows you to print out this pdf (without this header page) and tick off the parts as they come off the printer. Hopefully you won’t double print when you don’t want to.

Future Improvements to this doc
3) Add time of print using a Prusa mini as a guide.
4) Add AA (anti-aliasing) to images using gimp and scripts

NB thanks for all the great ideas. Even if I have not had time (yet) to implement them all. They are much appreciated. Any other ideas or comments please visit old.reddit.com/r/VORONDesign

Notes
This is fan base documentation. The official document take precedence in any conflict of information or technical detail.

Silly quote
May your Voron print head always fly “straight and true”, never tire and crash the bed for a sleep.

Picture	Details	Page	Comment
	Directory / STLs/Gantry/AB_Drive_Units / Filename / a_drive_frame_upper.stl / Manual name / A drive	26 / Done? / ▢ Yes	And / so it begins
	Directory / STLs/Gantry/Front_Idlers / Filename / [a]_tensioner_left.stl / Manual name / none found	27 / Done? / ▢ Yes	NB Page 27 / “Look for asterix next to the part. / It indicates that this is an accent part.” / Except * is not a good character in a file name, so they changed it to / Files starting with [a]
	Directory / STLs/Gantry/Front_Idlers / Filename / [a]_tensioner_right.stl / Manual name / none found	27 / Done? / ▢ Yes	Joke alert / Don’t print part / rm * / If you have no idea what I am talking about please ignore this note
	Directory / STLs/Gantry/Front_Idlers / Filename / front_idler_a_x2.stl / Manual name / A idler	28 / Done? / ▢ Yes	x2
	Directory / STLs/Gantry/Front_Idlers / Filename / front_idler_b_x2.stl / Manual name / none found	28 / Done? / ▢ Yes	x2
	Directory / STLs/Gantry/AB_Drive_Units / Filename / a_drive_frame_lower.stl / Manual name / A drive	34 / Done? / ▢ Yes
	Directory / STLs/Tools / Filename / AB_pulley_jig.stl / Manual name / none found	35 / Done? / ▢ Yes	tool
	Directory / STLs/Gantry/AB_Drive_Units / Filename / b_drive_frame_lower.stl / Manual name / B drive	37 / Done? / ▢ Yes
	Directory / STLs/Gantry/AB_Drive_Units / Filename / b_drive_frame_upper.stl / Manual name / B drive	38 / Done? / ▢ Yes
	T-Nuts M5 / AKA / “Roll in” T nuts	44 / Done? / ▢ Yes	They don’t have to go into the end. / They can be “rolled in”. / No need to disassemble frame.
	Warning / Lone M3 on page. / Pretending to be M5	44 / Done? / ▢ Yes	Beware Of / of the lone / lone M3 T-nut. Which I read as an M5 and had to get it back out.
	Directory / STLs/Gantry/AB_Drive_Units / Filename / [a]_y_endstop_bumper.stl / Manual name / End stop	50 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_rear_extrusionbracket_left.stl / Manual name / Rear brace	53 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_rear_extrusionbracket_right.stl / Manual name / Rear brace	55 / Done? / ▢ Yes
	Directory / STLs/Tools / Filename / MGN9_rail_guide_x2.stl / Manual name / Guide	58 / Done? / ▢ Yes	x2
	Directory / STLs/Z_Assembly / Filename / z_carriage_rear_3hole.stl / Manual name / Generic Cable Chain	64 / Done? / ▢ Yes	Check directory for 2 hole version if required / on cable chain
	Directory / STLs/Z_Assembly / Filename / z_stepper_rear.stl / Manual name / none found	65 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / [a]_z_rail_stop_x3.stl / Manual name / none found	68 / Done? / ▢ Yes	x3
	Directory / STLs/Z_Assembly / Filename / z_stepper_left.stl / Manual name / none found	69 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_stepper_right.stl / Manual name / none found	73 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_carriage_left.stl / Manual name / Left Z joint	77 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / [a]_z_carriage_left.stl / Manual name / none found	77 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / [a]_z_carriage_right.stl / Manual name / none found	79 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_carriage_right.stl / Manual name / none found	79 / Done? / ▢ Yes
	Directory / STLs/Skirt / Filename / corner_a_x2.stl / Manual name / Feet	90 / Done? / ▢ Yes	x2
	Directory / STLs/Skirt / Filename / corner_b_x2.stl / Manual name / Feet	90 / Done? / ▢ Yes	x2
	Directory / STLs/Skirt / Filename / [a]_corner_baseplate_a_x2.stl / Manual name / none found	90 / Done? / ▢ Yes	x2
	Directory / STLs/Skirt / Filename / [a]_corner_baseplate_b_x2.stl / Manual name / none found	90 / Done? / ▢ Yes	x2
	Page 99 has been ignored for the purposes of this doco . It is an overview or copy of the pic on 98. Also it has way too many parts on it. Normal service to resume		Page ignored
	Directory / STLs/Gantry/X_Axis/X_Carriage / Filename / probe_retainer_bracket.stl / Manual name / none found	100 / Done? / ▢ Yes	Note: There are two similar shapes. The one displayed and the 9mm one. / probe_retainer_bracket_9mm.st / But which one? / See below
	Which probe_retainer_bracket.stl? / This all depends on your probe see page 111 / After putting my X carriage together on page 110, my probe was flush with the X carriage. / I decided to go with the standard probe_retainer_bracket.stl / Seem to work fine.	Info only	My probe from the formbot kit was a Omron TL-Q5MMC2-Z / It was flush with the X carriage. / when it was assembled
	Directory / STLs/Gantry/X_Axis/X_Carriage / Filename / x_carriage_frame_left.stl / Manual name / X Carriage	100 / Done? / ▢ Yes	I had to gently sand the top of this part so it would mate properly
	Directory / STLs/Gantry/X_Axis/X_Carriage / Filename / x_carriage_frame_right.stl / Manual name / X Carriage	100 / Done? / ▢ Yes	I had to gently sand the top of this part so it would mate properly
	Directory / STLs/Gantry/X_Axis/XY_Joints / Filename / [a]_xy_joint_cable_bridge_3hole.stl / Manual name / none found	100 / Done? / ▢ Yes	Note: Check directory for 2 hole version if required for cable chain / Mine’s a 3 hole
	Directory / STLs/Gantry/X_Axis/XY_Joints / Filename / xy_joint_right_upper_MGN12.stl / Manual name / Right XY Joint	101 / Done? / ▢ Yes	NB if you are using a brim to prevent ABS warping you may have to remove it round the crevice outlined below
	Notes / Crevice outlined in blue on Right XY Joint. May need to be “cleaned out” with a craft knife if you have printed with a brim.	Info only
	Directory / STLs/Gantry/X_Axis/XY_Joints / Filename / xy_joint_right_lower_MGN12.stl / Manual name / Right XY Joint	102 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/XY_Joints / Filename / xy_joint_left_upper_MGN12.stl / Manual name / Left XY Joint	105 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/XY_Joints / Filename / xy_joint_left_lower_MGN12.stl / Manual name / Left XY Joint	106 / Done? / ▢ Yes
	Directory / STLs/Tools / Filename / MGN12_rail_guide_x2.stl / Manual name / none found	113 / Done? / ▢ Yes	x2
	Non printable part. / Thermal fuse	129	Please skip. Non printable part.
	Directory / STLs/Z_Assembly / Filename / nozzle_probe.stl / Manual name / none found	130 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_bed_left.stl / Manual name / none found	134 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_bed_rear.stl / Manual name / none found	136 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_bed_right.stl / Manual name	138 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage/Direct Feed / Filename / extruder_motor_plate.stl / Manual name / none found	146 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage/ / Direct Feed / Filename / chain_anchor_3hole.stl / Manual name / none found	146 / Done? / ▢ Yes	Check directory for 2 hole version if required
	Directory / STLs/Gantry/X_Axis/X_Carriage/ / Direct Feed / Filename / [a]_latch_shuttle.stl / Manual name / none found	146 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage/ / Direct Feed / Filename / extruder_body.stl / Manual name / none found	147 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage/Toolheads/Dragon / Filename / printhead_front_dragon.stl / Manual name / none found	148 / Done? / ▢ Yes	DRAGON mount / DO YOU HAVE A DRAGON hot end?
	Directory / STLs/Gantry/X_Axis/X_Carriage/Toolheads/Dragon / Filename / printhead_rear_dragon.stl / Manual name / none found	149 / Done? / ▢ Yes	DRAGON mount / DO YOU HAVE A DRAGON hot end?
	Directory / STLs/Gantry/X_Axis/X_Carriage/Direct Feed / Filename / [a]_latch.stl / Manual name / none found	161 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage/Direct Feed / Filename / [a]_guidler.stl / Manual name / none found	161 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage/Direct Feed / Filename / [a]_connector_cover.stl / Manual name / none found	163 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage / Filename / blower_housing_rear.stl / Manual name / none found	166 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage / Filename / hotend_fan_mount.stl / Manual name / none found	166 / Done? / ▢ Yes
	Directory / STLs/Gantry/X_Axis/X_Carriage / Filename / [a]_blower_housing_front.stl / Manual name / none found	167 / Done? / ▢ Yes
	Directory / STLs/Z_Assembly / Filename / z_cable_chain_mount_3hole.stl / Manual name / Z chain Anchor	173 / Done? / ▢ Yes	Check directory for 2 hole version if required
	Directory / STLs/Panels / Filename / wire_corner_left.stl / Manual name / cable cover	175 / Done? / ▢ Yes
	Directory / STLs/Panels / Filename / wire_corner_right.stl / Manual name / none found	176 / Done? / ▢ Yes
	Directory / STLs/Panels / Filename / deck_support_4mm_x8.stl / Manual name / Deck support	178 / Done? / ▢ Yes	X 8 / NB there are two variants 4mm and 3mm / deck_support_3mm_x8.stl
	Directory / STLs/ElectronicsBay / Filename / DIN_center_support_x2.stl / Manual name / none found	181 / Done? / ▢ Yes	x2
	Directory / STLs/ElectronicsBay / Filename / DIN_frame_mount_x4.stl / Manual name / none found	181 / Done? / ▢ Yes	x4
	Directory / STLs/ElectronicsBay / Filename / cable_frame_anchor_x6.stl / Manual name / none found	185 / Done? / ▢ Yes	X6
	Directory / STLs/ElectronicsBay / Filename / pcb_din_clip_v2_x5.stl / Manual name / none foundy	189 / Done? / ▢ Yes	x5
	Directory / STLs/ElectronicsBay / Filename / raspberrypi_bracket.stl / Manual name / none found	189 / Done? / ▢ Yes
	Directory / STLs/ElectronicsBay / Filename / rs25_psu_bracket.stl / Manual name / RS25-5 PSU	191 / Done? / ▢ Yes
	Directory / STLs/ElectronicsBay/ Controller_Mounds / Filename / Octopus_bracket_2pc.stl / Manual name / Controller Boar	193 / Done? / ▢ Yes	Note: do you have a Octopus? Other mounts in this directory include Duet, GTR,SKR,Spider etc
	Directory / STLs/Skirt / Filename / power_inlet_filtered.stl / Manual name / none found	195 / Done? / ▢ Yes
	Directory / STLs/ElectronicsBay / Filename / PSU_stabilizer_50mm.stl / Manual name / none found	198 / Done? / ▢ Yes
	Not a printed part. / Skip	199	Not printed part. / Skip
	Directory / STLs/Gantry/X_Axis/XY_Joints / Filename / [a]_endstop_pod_microswitch.stl / Manual name / none found	203 / Done? / ▢ Yes
	Directory / STLs/Gantry/AB_Drive_Units / Filename / [a]_y_endstop_housing.stl / Manual name / Not mentioned	Page not found / Done? / ▢ Yes	Warning / We could not find this part in the official manual but it’s in the STLs. / Additionally, the Y endstop is held within the [a]_endstop_pod_microswitch.stl part
	Directory / STLs/Gantry/AB_Drive_Units / Filename / [a]_wire_cover.stl / Manual name / none found	225 / Done? / ▢ Yes
	Directory / STLs/Skirt / Filename / side_fan_support_x2.stl / Manual name / none found	233 / Done? / ▢ Yes	x2
	Directory / STLs/Skirt / Filename / keystone_panel.stl / Manual name / none found	233 / Done? / ▢ Yes
	Directory / STLs/Skirt/250 / Filename / front_skirt_a_250.stl / Manual name / none found	233 / Done? / ▢ Yes	WARNING / 250mm x 250mm / do you have this bed size?
	Directory / STLs/Skirt/250 / Filename / front_skirt_b_250.stl / Manual name / none found	233 / Done? / ▢ Yes	WARNING / 250mm x 250mm / do you have this bed size?
	Directory / STLs/Skirt / Filename / [a]_mini12864_case_front_insert.stl / Manual name / none found	234
	Directory / STLs/Skirt / Filename / mini12864_case_front.stl / Manual name / none found	234 / Done? / ▢ Yes
	Directory / STLs/Skirt / Filename / mini12864_case_rear.stl / Manual name / none found	235 / Done? / ▢ Yes
	Warning: Joke detected / Can’t find the round thing, / You make my heart sing, / Wild thing. / You make everything groovie. / ABS mainly.	235	Not stl part / Please skip.
	Directory / STLs/Skirt / Filename / [a]_mini12864_case_hinge.stl / Manual name / none found	236 / Done? / ▢ Yes
	Directory / STLs/Skirt / Filename / [a]_keystone_blank_insert_x2.stl / Manual name / none found	237 / Done? / ▢ Yes	x2
	Directory / STLs/Skirt / Filename / [a]_skirt_logo_x2.stl / Manual name / none found	237 / Done? / ▢ Yes	X2
	Directory / STLs/Skirt / Filename / rear_center_skirt_250.stl / Manual name / none found	241 / Done? / ▢ Yes	WARNING / 250mm x 250mm / do you have this bed size?
	Directory / STLs/Skirt/250 / Filename / side_skirt_a_250_x2.stl / Manual name / none found	242 / Done? / ▢ Yes	WARNING / 250mm x 250mm / do you have this bed size? / x2
	Directory / STLs/Skirt/250 / Filename / side_skirt_b_250_x2.stl / Manual name / none found	242 / Done? / ▢ Yes	WARNING / 250mm x 250mm / do you have this bed size? / x2
	Directory / STLs/Skirt / Filename / [a]_60mm_fan_blank_insert_x2.stl / Manual name / none found	244 / Done? / ▢ Yes	x2
	Directory / STLs/Panels / Filename / bottom_panel_clip_x4.stl / Manual name / none found	250 / Done? / ▢ Yes	x4
	Directory / STLs/Panels / Filename / bottom_panel_hinge_x2.stl / Manual name / none found	250 / Done? / ▢ Yes	x2
	Directory / STLs/Panels / Filename / corner_panel_clip_4mm_x8.stl / Manual name / none found	254 / Done? / ▢ Yes	Warning 4mm or 6mm part? / x8
	Directory / STLs/Panels / Filename / midspan_panel_clip_4mm_x7.stl / Manual name / none found	254 / Done? / ▢ Yes	Warning 4mm or 6mm part? / x7
	Directory / STLs/Panels/Front_Doors / Filename / latch_x2.stl / Manual name / none found	263 / Done? / ▢ Yes	x2
	Directory / STLs/Panels/Front_Doors / Filename / handle_a_x2.stl / Manual name / none found	263 / Done? / ▢ Yes	x2
	Directory / STLs/Panels/Front_Doors / Filename / handle_b_x2.stl / Manual name / none found	263 / Done? / ▢ Yes	x2
	Directory / STLs/Panels/Front_Doors / Filename / door_hinge_x6.stl / Manual name / none found	265 / Done? / ▢ Yes	x6
	Directory / STLs/Exhaust_Filter / Filename / exhaust_filter_housing.stl / Manual name / none found	268 / Done? / ▢ Yes
	Directory / STLs/Exhaust_Filter / Filename / [a]_filter_access_cover.stl / Manual name / none found	270 / Done? / ▢ Yes
	Directory / STLs/Exhaust_Filter / Filename / [a]_exhaust_filter_mount_x2.stl / Manual name / none found	272 / Done? / ▢ Yes	x2
	Directory / STLs/Exhaust_Filter / Filename / exhaust_filter_grill.stl / Manual name / none found	272 / Done? / ▢ Yes
	Directory / STLs/Exhaust_Filter / Filename / bowen_retainer.stl / Manual name / none found	275 / Done? / ▢ Yes
	Directory / STLs/Exhaust_Filter / Filename / spool_holder.stl / Manual name / none found	276 / Done? / ▢ Yes
	Steve / (Team member and person who “drove the bus home on Trident project”)	280 / Done? / ▢ Yes	Man in the red shirt. Well reddish. / It’s in that spectrum
	Eddie / (Team member)	280 / Done? / ▢ Yes	This is not a red shirt.
	Dunar / (Team member)	280 / Done? / ▢ Yes	Support structure may be required for the beard.
	[a]_Russiancatfood.stl / Manual name / Maks Zolin	280 / Done? / ▢ Yes	May require multiple materials / Fearless leader

Done!

I have one question for you.

Did you print the tool on page 58 in the accent colour?

▢ Yes, because it’s cool

▢ No, Mr George, Because I am on to you

Place ✓ above

Note: I spent far too much time on this doco. I can only imagine the hard work that the Voron team has put into actually making the printer itself. So from a personal point of view I would like to say thanks to the official team here.