Title	Trident_1-9_complementary_3dPartsBuild_doco (Proposed future filename)
File name	Voron_1.9_3dprinting_guide.pdf (You put . In a filename?)
Date	2021-12-15 AM drop 2 (Unofficial version number)
Copy-rite	None. Free domain. Be free. Fly my pretties. FLY!
Warranty	None. Use at own risk. For entertainment purposes only.
Author(s)	Stephen George (Original idea and creation)
Claudermilk (Major proof read and error checking)

Introduction
Use this guide to print the parts as you need them, possibly the night before.

Latest version?
I tend to rush the first draft out and let everyone complain. To get the latest version of this document please goto url below and check the date.

https://github.com/LesserSpottedAustralianSquirel/voron_trident_pics/blob/main/Voron_1.9_trident_3dprinting_guide.pdf

Print parameters (More details on page 4 of official Trident manual)
Material ABS, Infill gyroid, Infill 40% Layer_height 0.2mm, Wall_count 4, Top/bottom layers 5, Nossle/Nozzle 0.4mm

NB: Many of the Voron parts “mate” together. Therefore the top needs to be quite smooth. I found that a light sand papering helped allow these parts to mate. Another idea maybe to enable “ironing” in your slicer.
NB: I used a Prusa mini to print the parts in ABS. I had to use a brim to prevent warping. While the brim came off easily I had to use a plumbers deburring tool (from the hardware shop) and sometimes a craft knife to remove the elephants foot like effect.

The Rules
The first time a picture of a part is shown in the official instructions it should be added to the list below, along with the page number. After that it’s ignored as you should have already printed it.

The Machine the parts are for
Building Formbot kit, 250 x 250, Direct feed, Dragon High Flow, 3 hole cable chain.

Keeping track
The Printed ▢ tick box, under the picture, allows you to print out this pdf and tick off the parts as they come off the printer. Hopefully you won’t double print when you don’t want to.

Future Improvements to this doc
3) Add time of print using a Prusa mini as a guide.
4) Add AA (anti-aliasing) to images using gimp and scripts

NB thanks for all the great ideas. Even if I have not had time (yet) to implement them all. They are much appreciated. Any other ideas or comments please visit old.reddit.com/r/VORONDesign

Notes
This is fan base documentation. The official document take precedence in any conflict of information or technical detail.

Picture	Details	Page	Comment
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / a_drive_frame_upper / Manual name / A drive	26	And / so it begins
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / [a]_tensioner_left / Manual name / none found	27	NB Page 27 / “Look for asterix next to the part. / It indicates that this is an accent part.” / Except * is not a good character in a file name, so they changed it to / Files starting with [a]
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / [a]_tensioner_right / Manual name / none found	27	Joke alert / Don’t print part / rm * / If you have no idea what I am talking about please ignore this note
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / front_idler_a_x2 / Manual name / A idler	28	x2
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / front_idler_b_x2 / Manual name / none found	28	x2
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / a_drive_frame_lower / Manual name / A drive	34
Printed? / ▢	Directory / STLs/Tools / Filename / AB_pulley_jig / Manual name / none found	35	tool
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / b_drive_frame_lower / Manual name / B drive	37
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / b_drive_frame_upper / Manual name / B drive	38
	T-Nuts M5 / AKA / “Roll in” T nuts	44	They don’t have to go into the end. / They can be “rolled in”. / No need to disassemble frame.
	Warning / Lone M3 on page. / Pretending to be M5	44	Beware Of / of the lone / lone M3 T-nut. Which I read as an M5 and had to get it back out.
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / [a]_y_endstop_bumper / Manual name / End stop	50
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_rear_extrusionbracket_left / Manual name / Rear brace	53
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_rear_extrusionbracket_right / Manual name / Rear brace	55
Printed? / ▢	Directory / STLs/Tools / Filename / MGN9_rail_guide_x2 / Manual name / Guide	58	x2
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_carriage_rear_3hole / Manual name / Generic Cable Chain	64	Check directory for 2 hole version if required / on cable chain
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_stepper_rear / Manual name / none found	65
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / [a]_z_rail_stop_x3 / Manual name / none found	68	x3
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_stepper_left / Manual name / none found	69
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_stepper_right / Manual name / none found	73
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_carriage_left / Manual name / Left Z joint	77
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / [a]_z_carriage_left / Manual name / none found	77
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / [a]_z_carriage_right / Manual name / none found	79
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_carriage_right / Manual name / none found	79
Printed? / ▢	Directory / STLs/Skirt / Filename / corner_a_x2 / Manual name / Feet	90	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / corner_b_x2 / Manual name / Feet	90	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_corner_baseplate_a_x2 / Manual name / none found	90	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_corner_baseplate_b_x2 / Manual name / none found	90	x2
	Page 99 has been ignored for the purposes of this doco . It is an overview or copy of the pic on 98. Also it has way too many parts on it. Normal service to resume		Page ignored
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / probe_retainer_bracket / Manual name / none found	100	Note: There are two similar shapes. The one displayed and the 9mm one. / probe_retainer_bracket_9mm.st / But which one? / See below
	Which probe_retainer_bracket? / This all depends on your probe see page 111 / After putting my X carriage together on page 110, my probe was flush with the X carriage. / I decided to go with the standard probe_retainer_bracket / Seem to work fine.	Info only	My probe from the formbot kit was a Omron TL-Q5MMC2-Z / It was flush with the X carriage. / when it was assembled
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / x_carriage_frame_left / Manual name / X Carriage	100	I had to gently sand the top of this part so it would mate properly
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / x_carriage_frame_right / Manual name / X Carriage	100	I had to gently sand the top of this part so it would mate properly
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / [a]_xy_joint_cable_bridge_3hole / Manual name / none found	100	Note: Check directory for 2 hole version if required for cable chain / Mine’s a 3 hole
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_right_upper_MGN12 / Manual name / Right XY Joint	101	NB if you are using a brim to prevent ABS warping you may have to remove it round the crevice outlined below
	Notes / Crevice outlined in blue on Right XY Joint. May need to be “cleaned out” with a craft knife if you have printed with a brim.	Info only
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_right_lower_MGN12 / Manual name / Right XY Joint	102
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_left_upper_MGN12 / Manual name / Left XY Joint	105
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_left_lower_MGN12 / Manual name / Left XY Joint	106
Printed? / ▢	Directory / STLs/Tools / Filename / MGN12_rail_guide_x2 / Manual name / none found	113	x2
	Non printable part. / Thermal fuse	129	Please skip. Non printable part.
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / nozzle_probe / Manual name / none found	130
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_bed_left / Manual name / none found	134
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_bed_rear / Manual name / none found	136
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_bed_right / Manual name	138
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / extruder_motor_plate / Manual name / none found	146
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/ / Direct Feed / Filename / chain_anchor_3hole / Manual name / none found	146	Check directory for 2 hole version if required
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/ / Direct Feed / Filename / [a]_latch_shuttle / Manual name / none found	146
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/ / Direct Feed / Filename / extruder_body / Manual name / none found	147
Printed? / ▢	Directory / STLs/Gantry/X_Axis/X_Carriage/Toolheads/Dragon / Filename / printhead_front_dragon / Manual name / none found	148	DRAGON mount / DO YOU HAVE A DRAGON hot end?
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Toolheads/Dragon / Filename / printhead_rear_dragon / Manual name / none found	149	DRAGON mount / DO YOU HAVE A DRAGON hot end?
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / [a]_latch / Manual name / none found	161
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / [a]_guidler / Manual name / none found	161
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / [a]_connector_cover / Manual name / none found	163
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / blower_housing_rear / Manual name / none found	166
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / hotend_fan_mount / Manual name / none found	166
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / [a]_blower_housing_front / Manual name / none found	167
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_cable_chain_mount_3hole / Manual name / Z chain Anchor	173	Check directory for 2 hole version if required
Printed? / ▢	Directory / STLs/Panels / Filename / wire_corner_left / Manual name / cable cover	175
Printed? / ▢	Directory / STLs/Panels / Filename / wire_corner_right / Manual name / none found	176
Printed? / ▢	Directory / STLs/Panels / Filename / deck_support_4mm_x8 / Manual name / Deck support	178	X 8 / NB there are two variants 4mm and 3mm / deck_support_3mm_x8
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / DIN_center_support_x2 / Manual name / none found	181	x2
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / DIN_frame_mount_x4 / Manual name / none found	181	x4
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / cable_frame_anchor_x6 / Manual name / none found	185	X6
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / pcb_din_clip_v2_x5 / Manual name / none foundy	189	x5
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / raspberrypi_bracket / Manual name / none found	189
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / rs25_psu_bracket / Manual name / RS25-5 PSU	191
Printed? / ▢	Directory / STLs/ElectronicsBay/ Controller_Mounds / Filename / Octopus_bracket_2pc / Manual name / Controller Boar	193	Note: do you have a Octopus? Other mounts in this directory include Duet, GTR,SKR,Spider etc
Printed? / ▢	Directory / STLs/Skirt / Filename / power_inlet_filtered / Manual name / none found	195
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / PSU_stabilizer_50mm / Manual name / none found	198
	Not a printed part. / Skip	199	Not printed part. / Skip
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / [a]_endstop_pod_microswitch / Manual name / none found	203
Printed? / ▢	Directory / STLs/Gantry/ / AB_Drive_Units / Filename / [a]_y_endstop_housing / Manual name / Not mentioned	Page not found	Warning / We could not find this part in the official manual but it’s in the STLs. / Additionally, the Y endstop is held within the [a]_endstop_pod_microswitch part
Printed? / ▢	Directory / STLs/Gantry/ / AB_Drive_Units / Filename / [a]_wire_cover / Manual name / none found	225
Printed? / ▢	Directory / STLs/Skirt / Filename / side_fan_support_x2 / Manual name / none found	233	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / keystone_panel / Manual name / none found	233
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / front_skirt_a_250 / Manual name / none found	233	WARNING / 250mm x 250mm / do you have this bed size?
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / front_skirt_b_250 / Manual name / none found	233	WARNING / 250mm x 250mm / do you have this bed size?
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_mini12864_case_front_insert / Manual name / none found	234
Printed? / ▢	Directory / STLs/Skirt / Filename / mini12864_case_front / Manual name / none found	234
Printed? / ▢	Directory / STLs/Skirt / Filename / mini12864_case_rear / Manual name / none found	235
	Warning: Joke detected / Can’t find the round thing, / You make my heart sing, / Wild thing. / You make everything groovie. / ABS mainly.	235	Not stl part / Please skip.
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_mini12864_case_hinge / Manual name / none found	236
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_keystone_blank_insert_x2 / Manual name / none found	237	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_skirt_logo_x2 / Manual name / none found	237	X2
Printed? / ▢	Directory / STLs/Skirt / Filename / rear_center_skirt_250 / Manual name / none found	241	WARNING / 250mm x 250mm / do you have this bed size?
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / side_skirt_a_250_x2 / Manual name / none found	242	WARNING / 250mm x 250mm / do you have this bed size? / x2
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / side_skirt_b_250_x2 / Manual name / none found	242	WARNING / 250mm x 250mm / do you have this bed size? / x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_60mm_fan_blank_insert_x2 / Manual name / none found	244	x2
Printed? / ▢	Directory / STLs/Panels / Filename / bottom_panel_clip_x4 / Manual name / none found	250	x4
Printed? / ▢	Directory / STLs/Panels / Filename / bottom_panel_hinge_x2 / Manual name / none found	250	x2
Printed? / ▢	Directory / STLs/Panels / Filename / corner_panel_clip_4mm_x8 / Manual name / none found	254	Warning 4mm or 6mm part? / x8
Printed? / ▢	Directory / STLs/Panels / Filename / midspan_panel_clip_4mm_x7 / Manual name / none found	254	Warning 4mm or 6mm part? / x7
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / latch_x2 / Manual name / none found	263	x2
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / handle_a_x2 / Manual name / none found	263	x2
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / handle_b_x2 / Manual name / none found	263	x2
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / door_hinge_x6 / Manual name / none found	265	x6
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / exhaust_filter_housing / Manual name / none found	268
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / [a]_filter_access_cover / Manual name / none found	270
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / [a]_exhaust_filter_mount_x2 / Manual name / none found	272	x2
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / exhaust_filter_grill / Manual name / none found	272
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / bowen_retainer / Manual name / none found	275
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / spool_holder / Manual name / none found	276
Printed? / ▢	Steve / (Team member and person who “drove the bus home on Trident project”)	280	Man in the red shirt. Well reddish. / It’s in that spectrum
Printed? / ▢	Eddie / (Team member)	280	This is not a red shirt.
Printed? / ▢	Dunar / (Team member)	280	Support structure may be required for the beard.
Printed? / ▢	[a]_Russiancatfood / Manual name / Maks Zolin	280	May require multiple materials / Fearless leader

Done!

I have one question for you.

Did you print the tool on page 58 in the accent colour?

▢ Yes, because it’s cool

▢ No, Mr George, Because I am on to you

Place ✓ above

Note: I spent far too much time on this doco. I can only imagine the hard work that the Voron team has put into actually making the printer itself. So from a personal point of view I would like to say thanks to the official team here.