Title	Trident_1-9_complementary_3dPartsBuild_doco (Proposed future filename)
File name	Voron_1.9_3dprinting_guide.pdf (You put . In a filename?)
Date	2021-12-17 (Unofficial version number)
Copy-rite	None. Free domain. Be free. Fly my pretties. FLY!
Warranty	None. Use at own risk. For entertainment purposes only.
Authors	Stephen George, Claudermilk (Major proof read and error checking)

Introduction
Use this guide to print the parts as you need them, possibly the night before.

Latest version?
I tend to rush the first draft out. To get the latest V. Goto URL below and check the date.
https://github.com/LesserSpottedAustralianSquirel/voron_trident_pics/blob/main/Voron_1.9_trident_3dprinting_guide.pdf

Print parameters (More details on page 4 of official Trident manual)
Material ABS, Infill gyroid, Infill 40% Layer_height 0.2mm, Wall_count 4, Top/bottom layers 5, Nossle/Nozzle 0.4mm

My prints: (for Prusa mini): Brim yes 5mm, Ironing yes, first layer 10 mm/s, infill grid
NB: Many of the Voron parts “mate” together. I found that a light sand papering helped allow these parts to mate. Another idea: enable “ironing” in your slicer. (update :“oh yeah”).
NB: I used a Prusa mini (bed flinger) to print parts & had to use a plumbers deburring tool (from hardware shop) & sometimes a craft knife, to remove the elephants foot like effect and brim.

The Rules
The first time a picture of a part is shown in the official instructions it’s added to the list. After that it’s ignored as you should have already printed it.

The Machine the parts are for
Building Formbot kit, 250 x 250, Direct feed, Dragon High Flow, 3 hole cable chain.

Keeping track
The Printed ▢ tick box, under the picture, allows you to print out this pdf and tick off the parts as they come off the printer. Anyone know how to make them PDF tick able? So we don’t have to print doco out, but can just tick and save the electronic PDF to keep track?

Future Improvements to this doc
3) Add time of print using a Prusa mini as a guide.
4) Add AA (anti-aliasing) to images using gimp and scripts

Thanks for all the great ideas. Even if I have not had time (yet) to implement them all.
 https://old.reddit.com/r/VORONDesign/comments/rc8wcb/voron_trident_printing_guide_very_very_draft_and/

Notes
This is fan base documentation. The official document take precedence in any conflict of information or technical detail.

Picture	Details	Comment
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / a_drive_frame_upper / Page Number / 26	And / so it begins
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / [a]_tensioner_left / Page number / 27	NB Page 27 / “Look for asterix next to the part. / It indicates that this is an accent part.” / Except * is not a good character in a file name, so they changed it to / Files starting with [a]
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / [a]_tensioner_right / Page number / 27	Joke alert / Don’t print part / rm * / If you have no idea what I am talking about please ignore this note
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / front_idler_a_x2 / Page number / 28	x2
Printed? / ▢	Directory / STLs/Gantry/ / Front_Idlers / Filename / front_idler_b_x2 / Page number / 28	x2
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / a_drive_frame_lower / Page number / 34
Printed? / ▢	Directory / STLs/Tools / Filename / AB_pulley_jig / Page number / 35	Tool
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / b_drive_frame_lower / Page number / 37
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / b_drive_frame_upper / Page number / 38
	T-Nuts M5 / AKA / “Roll in” T nuts / Page number / 44	They don’t have to go into the end. / They can be “rolled in”. / No need to disassemble frame.
	Warning / Lone M3 on page. / Pretending to be M5 / Page number / 44	Beware Of / of the lone / lone M3 T-nut. Which I read as an M5 and had to get it back out.
Printed? / ▢	Directory / STLs/Gantry/AB_Drive_Units / Filename / [a]_y_endstop_bumper / Page number / 50
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_rear_extrusionbracket_left / Page number / 53
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_rear_extrusionbracket_right / Page number / 55
Printed? / ▢	Directory / STLs/Tools / Filename / MGN9_rail_guide_x2 / Page number / 58	x2
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_carriage_rear_3hole / Page number / 64	Check directory for 2 hole version if required / on cable chain
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_stepper_rear / Page number / 65
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / [a]_z_rail_stop_x3 / Page number / 68	x3
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_stepper_left / Page number / 69
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_stepper_right / Page number / 73
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_carriage_left / Page number / 77
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / [a]_z_carriage_left / Page number / 77
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / [a]_z_carriage_right / Page number / 79
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_carriage_right / Page number / 79
Printed? / ▢	Directory / STLs/Skirt / Filename / corner_a_x2 / Page number / 90	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / corner_b_x2 / Page number / 90	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_corner_baseplate_a_x2 / Page number / 90	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_corner_baseplate_b_x2 / Page number / 90	x2
	Page 99 has been ignored for the purposes of this doco . It is an overview or copy of the pic on 98. Also it has way too many parts on it. Normal service to resume	Page ignored
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / probe_retainer_bracket / Page number / 100	Note: There are two similar shapes. The one displayed and the 9mm one. / probe_retainer_bracket_9mm.st / But which one? / See below
	Which probe_retainer_bracket? / This all depends on your probe see page 111 / After putting my X carriage together on page 110, my probe was flush with the X carriage. / I decided to go with the standard probe_retainer_bracket. / It seem to work fine.	My probe from the formbot kit was a Omron TL-Q5MMC2-Z / It was flush with the X carriage when it was assembled
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / x_carriage_frame_left / Page number / 100	I had to gently sand the top of this part so it would mate properly
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / x_carriage_frame_right / Page number / 100	I had to gently sand the top of this part so it would mate properly
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / [a]_xy_joint_cable_bridge_ / 3hole / Page number / 100	Note: Check directory for 2 hole version if required for cable chain / Mine’s a 3 hole
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_right_upper_MGN12 / Page number / 101	NB if you are using a brim to prevent ABS warping you may have to remove it round the crevice outlined below
	Notes / Crevice outlined in blue on Right XY Joint. May need to be “cleaned out” with a craft knife if you have printed with a brim.
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_right_lower_MGN12 / Page number / 102
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_left_upper_MGN12 / Page number / 105
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / xy_joint_left_lower_MGN12 / Page number / 106
Printed? / ▢	Directory / STLs/Tools / Filename / MGN12_rail_guide_x2 / Page number / 113	x2
	Page 116 / Missing screws. To be installed later. / Which page would they be installed later?	Will update when I know the answer. But for now I personally will be adding them. / Because I am a rebel. (Without a 3d printer) / I can always remove them.
	Installing the belt (page124) / The manual has you putting the belt on a single x_carriage_frame (from page 100). / The Youtube video however secured both belts with x_carriage_frame_left. / The belts are then threaded through the machine and then secured with the x_carriage_frame_right. / Only then are the x_carriage_frame_left and x_carriage_frame_right are then bolted together.	To my mind the Youtube way makes much more sense as you break the problem down into smaller tasks and you are not left holding 4 belt ends and screwing bolts in at the same time. / I did it the manual way successfully, but then I am good at holding things with my feet while simultaneously levitating. / Fortunately my screw driver was teeth safe.
The side edges were easy to line up but I started with a lip ie too soon and only found out once I have put the rest of the magnet at the end. Just thought I would mention it so you don’t make the same mistake.	Installing magnetic sheet. / But which side? The aluminium sheet has V holes cut into it for the V head of the screws. The manual seems to suggest. That side. Looks like I will have to drill from the other side to get the hole and then cut it out manually with a craft knife. I will update if this is wrong. / Page number / 127	Note: My magnetic sheet and aluminium sheet was a slight rectangle. If yours is to, make sure the long side of the magnetic sheet is matched to the long side of the aluminium sheet.
	Non printable part. / Thermal fuse / Page number / 129	Please skip. Non printable part.
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / nozzle_probe / Page number / 130
	Page number / 130 / I put the bottle opener in a vice and then used a long 3mm bolt in the in the GT2 for leverage and it just popped off.	“Apply the required force to fully / seat the pulley in the printed / part” / Right okay. Obviously your related to he-man. In the end I used a vice to get it in parallel.
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_bed_left / Page number / 134
	Page number / 134 / Snap fit for the GE5C bearing? I found a 8mm Roller skate bearing went nicely over the top of the GE5C bearing and protected the middle while I used a vice to push it in. Not recommending this, but it worked for me.
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_bed_rear / Page number / 136
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_bed_right / Page number / 138
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / extruder_motor_plate / Page number / 146
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/ / Direct Feed / Filename / chain_anchor_3hole / Page number / 146	Check directory for 2 hole version if required
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/ / Direct Feed / Filename / [a]_latch_shuttle / Page number / 146
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/ / Direct Feed / Filename / extruder_body / Page number / 147
Printed? / ▢	Directory / STLs/Gantry/X_Axis/X_Carriage/Toolheads/Dragon / Filename / printhead_front_dragon / Page number / 148	DRAGON mount / DO YOU HAVE A DRAGON hot end?
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Toolheads/Dragon / Filename / printhead_rear_dragon / Page number / 149	DRAGON mount / DO YOU HAVE A DRAGON hot end?
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / [a]_latch / Page number / 161
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / [a]_guidler / Page number / 161
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage/Direct Feed / Filename / [a]_connector_cover / Page number / 163
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / blower_housing_rear / Page number / 166
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / hotend_fan_mount / Page number / 166
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/X_Carriage / Filename / [a]_blower_housing_front / Page number / 167
Printed? / ▢	Directory / STLs/Z_Assembly / Filename / z_cable_chain_mount_3hole / Page number / 173	Check directory for 2 hole version if required
Printed? / ▢	Directory / STLs/Panels / Filename / wire_corner_left / Page number / 175
Printed? / ▢	Directory / STLs/Panels / Filename / wire_corner_right / Page number / 176
Printed? / ▢	Directory / STLs/Panels / Filename / deck_support_4mm_x8 / Page number / 178	X 8 / NB there are two variants 4mm and 3mm / deck_support_3mm_x8
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / DIN_center_support_x2 / Page number / 181	x2
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / DIN_frame_mount_x4 / Page number / 181	x4
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / cable_frame_anchor_x6 / Page number / 185	X6
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / pcb_din_clip_v2_x5 / Page number / 189	x5
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / raspberrypi_bracket / Page number / 189
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / rs25_psu_bracket / Page number / 191
Printed? / ▢	Directory / STLs/ElectronicsBay/ Controller_Mounts / Filename / Octopus_bracket_2pc / Page number / 193	Note: do you have a Octopus? Other mounts in this directory include Duet, GTR,SKR,Spider etc
Printed? / ▢	Directory / STLs/Skirt / Filename / power_inlet_filtered / Page number / 195
Printed? / ▢	Directory / STLs/ElectronicsBay / Filename / PSU_stabilizer_50mm / Page number / 198
	Not a printed part. / Skip / Page number / 199	Not printed part. / Skip
Printed? / ▢	Directory / STLs/Gantry/ / X_Axis/XY_Joints / Filename / [a]_endstop_pod_microswitch / Page number / 203
Printed? / ▢	Directory / STLs/Gantry/ / AB_Drive_Units / Filename / [a]_y_endstop_housing / Page number / Page not found	Warning / We could not find this part in the official manual but it’s in the STLs. / Additionally, the Y endstop is held within the [a]_endstop_pod_microswitch part
Printed? / ▢	Directory / STLs/Gantry/ / AB_Drive_Units / Filename / [a]_wire_cover / Page number / 225
Printed? / ▢	Directory / STLs/Skirt / Filename / side_fan_support_x2 / Page number / 233	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / keystone_panel / Page number / 233
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / front_skirt_a_250 / Page number / 233	WARNING / 250mm x 250mm / do you have this bed size?
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / front_skirt_b_250 / Page number / 233	WARNING / 250mm x 250mm / do you have this bed size?
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_mini12864_case_ / front_insert / Page number / 234
Printed? / ▢	Directory / STLs/Skirt / Filename / mini12864_case_front / Page number / 234
Printed? / ▢	Directory / STLs/Skirt / Filename / mini12864_case_rear / Page number / 235
	Warning: Joke detected / Can’t find the round thing, / You make my heart sing, / Wild thing. / You make everything groovie. / ABS mainly. / Page number / 235	Not stl part / Please skip.
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_mini12864_case_hinge / Page number / 236
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_keystone_blank_insert_x2 / Page number / 237	x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_skirt_logo_x2 / Page number / 237	X2
Printed? / ▢	Directory / STLs/Skirt / Filename / rear_center_skirt_250 / Page number / 241	WARNING / 250mm x 250mm / do you have this bed size?
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / side_skirt_a_250_x2 / Page number / 242	WARNING / 250mm x 250mm / do you have this bed size? / x2
Printed? / ▢	Directory / STLs/Skirt/250 / Filename / side_skirt_b_250_x2 / Page number / 242	WARNING / 250mm x 250mm / do you have this bed size? / x2
Printed? / ▢	Directory / STLs/Skirt / Filename / [a]_60mm_fan_blank_ / insert_x2 / Page number / 244	x2
Printed? / ▢	Directory / STLs/Panels / Filename / bottom_panel_clip_x4 / Page number / 250	x4
Printed? / ▢	Directory / STLs/Panels / Filename / bottom_panel_hinge_x2 / Page number / 250	x2
Printed? / ▢	Directory / STLs/Panels / Filename / corner_panel_clip_4mm_x8 / Page number / 254	Warning 4mm or 6mm part? / x8
Printed? / ▢	Directory / STLs/Panels / Filename / midspan_panel_clip_4mm_x7 / Page number / 254	Warning 4mm or 6mm part? / x7
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / latch_x2 / Page number / 263	x2
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / handle_a_x2 / Page number / 263	x2
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / handle_b_x2 / Page number / 263	x2
Printed? / ▢	Directory / STLs/Panels/ / Front_Doors / Filename / door_hinge_x6 / Page number / 265	x6
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / exhaust_filter_housing / Page number / 268
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / [a]_filter_access_cover / Page number / 270
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / [a]_exhaust_filter_mount_x2 / Page number / 272	x2
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / exhaust_filter_grill / Page number / 272
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / bowen_retainer / Page number / 275
Printed? / ▢	Directory / STLs/Exhaust_Filter / Filename / spool_holder / Page number / 276
Printed? / ▢	Steve / (Team member and person who “drove the bus home on Trident project”) / Page number / 280	Man in the red shirt. Well reddish. / It’s in that spectrum
Printed? / ▢	Eddie / (Team member) / Page number / 280	This is not a red shirt.
Printed? / ▢	Dunar / (Team member) / Page number / 280	Support structure may be required for the beard.
Printed? / ▢	Maks Zolin / AKA [a]_Russiancatfood / Glorious and fearless leader / Page number / 281	May require multiple materials to print.

Done!

I have one question for you.

Did you print the tool on page 58 in the accent colour?

▢ Yes, because it’s cool

▢ No, Mr George, Because I am on to you

Place ✓ above

Note: I spent far too much time on this doco. I can only imagine the hard work that the Voron team has put into actually making the printer itself. So from a personal point of view I would like to say thanks to the official team here.

Credits list

I suddenly realised that a lot of people had commented and given great suggestions to improve this doco and I had not given them their due credit. If I missed you, then opps. My bad. In my defence I fully expected this project to be ignored, So without further ado here is the list.

Credit	Condensed Request	Response
mapsedge	Bigger font please. I am getting older and the text is hard to read	I may have over compensated. Done as requested.
Claudermilk	Here are some things I would change	I think you have written more than me. Done as requested.
Appropriate_Rice3348	4mm nossil? That’s a big nozzle. Should mounds" be "mounts"?	Updated to 0.4mm nossle. Updated spelling.
imawsm_	anti-aliasing	Added to things to do
jpgadbois	I initially thought this was a guide to setting up printing parameters on a Trident rather than how to print parts for a Trident	Good point. Will update file name in git when (and If) I do the upcoming 1.10 Super trident.
mvrckcompany	What about removing the background from each of the part pictures? Add in some shadows to make it pop.	Background gone. Unfortunately adding shadow is beyond my limited knowledge
Leang	Color the accent parts differently in the thumbnails for easy visual difference.	Done as requested
imoftendisgruntled	I also think the manual could use a page at the front of every section that has a "For this section you will need:" header followed by pictures and filenames of the STLs along with the hardware bits from the BOM.	Good point. However I am simply following the official manual. But good point.
Castorreddit	Best way of doing this is not on reddit, but on github.	Thanks and done.

And Cut.